## Slide 1
Flight Data

## Slide 2
Nominal AoA = 0 deg
Nominal M = 3.4
1.4s, .3 r/s
5.6s, .1 r/s
Yancey64, page 27

## Slide 4
Inertia Products and Moments

## Slide 5
Jxz = -700 slug-ft2
Jxx = 3600 slug-ft2

## Slide 6
Jyy = 86000 slug-ft2

## Slide 7
Jzz = 88500 slug-ft2

## Slide 8
Forces: Lift, Drag, and Sideforce

## Slide 9
Walker60, pdf page 66
CLwb = 0
Digitized and integrated in simulation

## Slide 10
Walker60, pdf page 73
M=0
M=12
Wind tunnel is dashed line
CLAlpha_pdeg = 0.03
Digitized and integrated in simulation, but not used given CL data.

## Slide 11
Walker60, pdf page 73
M=0
M=12
CLdele_pdeg = 0.005
Digitized and integrated in simulation

## Slide 12
Digitized and integrated in simulation

## Slide 13
CDwb = 0.058
Saltzmann66, pdf page 31
Digitized and integrated in simulation

## Slide 14
Saltzmann66, pdf page 32
Digitized and integrated in simulation

## Slide 15
Digitized and integrated in simulation

## Slide 16
Digitized and integrated in simulation

## Slide 18
CDdele_pdeg=0
(Assumed zero)

## Slide 19
CDdelsb_pdeg=0
(Not included)

## Slide 20
CYBeta_pdeg = -0.02
M=2.0
M=12
Digitized and integrated in simulation

## Slide 21
CYP_prps = 0.017
M=2.0
M=12
Note, significant side force due to roll as AoA increases.
Digitized and integrated in simulation

## Slide 22
CYr_prps = -0.92
M=2.0
M=12
Assumed that CYbetadot_prps = 0
The effect of sidewash lag at the vertical tail is analyzed in
reference 50, in which it is shown that the derivatives are related
to the rate of change of sidewash angle with angle of sideslip as
follows... The sidewash variations at the tail , however, are not significant, and
the derivatives (CYbetadot and Cnbetadot) therefore have been dropped. – Walker 1960, page 32
Digitized and integrated in simulation

## Slide 23
CYdela_pdeg = -0.00030
M=2.0
M=12
Walker60, pdf page 115
Digitized and integrated in simulation

## Slide 24
Walker60, pdf page 113
CYdelr_pdeg = 0.0057
M=2.0
M=12
Digitized and integrated in simulation

## Slide 25
Moments: Roll

## Slide 26
ClBeta_pdeg = 0
M=2.0
M=12
Digitized and integrated in simulation

## Slide 27
ClP_prps = -0.185
M=2.0
M=12
Digitized and integrated in simulation

## Slide 28
ClR_prps = -0.08
Assumed Clbetadot_prps = 0
Digitized and integrated in simulation

## Slide 29
Cldela_pdeg = 0.0007
M=0.0
M=12
Digitized and integrated in simulation

## Slide 30
Cldelr_pdeg = 0.00025
Digitized and integrated in simulation

## Slide 31
Moments: Pitch

## Slide 32
Digitized and integrated in simulation

## Slide 33
Walker60, pdf page 75
CMAlpha_pdeg = -0.01
Digitized and integrated in simulation

## Slide 34
CMQ_prps = -4.4
M=2.0
M=12
Walker60, pdf page 84
Digitized and integrated in simulation

## Slide 35
Walker60, pdf page 84
Digitized and integrated in simulation

## Slide 36
Walker60, pdf page 84
Digitized and integrated in simulation

## Slide 37
Walker60, pdf page 84
Digitized and integrated in simulation

## Slide 38
Walker60, pdf page 84
CMAlphadot_prps = -0.1
M=2.0
M=12
Not Included in Simulation

## Slide 39
CMdele_pdeg = -0.008
Walker60, pdf page 77
Digitized and integrated in simulation

## Slide 40
CMdelsb_pdeg = 0

## Slide 41
Moments: Yaw

## Slide 42
CnBeta_pdeg = 0.0046
M=2.0
M=12
Digitized and integrated in simulation

## Slide 43
CnP_prps = -0.01
M=2.0
M=12
Digitized and integrated in simulation

## Slide 44
CnR_prps = -1.19
M=2.0
M=12
Assume Cnbetadot = 0
Digitized and integrated in simulation

## Slide 45
Cndela_pdeg = 0.00045
Digitized and integrated in simulation

## Slide 46
Cndelr_pdeg = -0.0039
M=0.0
M=12
Digitized and integrated in simulation